## Slide 1: RuckU 2013 on Tour
GT Hill & Eric Stresen-Reuter

## Slide 2: Housekeeping
Restrooms
Agenda
Tweet!
  #rucku
  @ericsr @gthill @ruckuswireless
Introductions

## Slide 3: Ruckus in 15
Company, Technology, and Update

## Slide 4: Fast and Fierce
Began Operations | 2004, Sunnyvale, CA
Status | Publicly held (NYSE: RKUS)
CEO | Selina Lo
Innovation | Carrier class Smart Wi-Fi
R&D Centers | Sunnyvale, China, Taiwan, India, Israel
2011/2012 Revenue | $120 million / $214.7 million (79% y/y)
4Q12 revenue | $62.2 million
CAGR | 64% (2009-2011)
Customers | 20,000+
Employees | 725+ in 33 countries
Patents | 60 granted (82 pending)
Markets | Carrier/enterprise wireless infrastructure
Chart: 
| 1st Qtr
Sales | 70 | 30
30%
70%
2012
CARRIER
ENTERPRISE
REVENUE

## Slide 5: Growing Share in the Enterprise
Chart: 
| 1st Qtr | 2nd Qtr | 3rd Qtr | 4th Qtr
Sales | 51 | 5 | 11 | 33
World’s Top Three WLAN Suppliers (4Q12)
(based on estimated revenue)
51%
33%
11%
5%
Cisco
Aruba
Ruckus
Others
Chart: 
| Category 1
Series 1 | 20
Series 2 | 33
Series 3 | 183.2
33%
20%
34%
Cisco
Aruba
65%
Worldwide WLAN Market Growth
(1Q11 to 4Q12)

## Slide 6: Outpacing the WLAN Market
Cisco
Aruba
VENDOR | Q1 2011 | Q2 2011 | Q3 2011 | Q4 2011 | Q1 2012 | Q2 2012 | Q3 2012 | Q4 2012 | % Change 1Q11-4Q12 | CQGR*
Cisco | 321.9 | 360 | 399.2 | 417.7 | 407.6 | 491.7 | 502.4 | 557.1 | 33% | 8.1%
Aruba | 77.9 | 79.1 | 79 | 93.7 | 105.5 | 110.5 | 114.6 | 123.3 | 20% | 6.7%
RUCKUS | 18.5 | 22.8 | 29.6 | 40.4 | 43 | 45.7 | 52.4 | 56.0 | 65% | 17.4%
TOTAL MARKET | 617 | 649 | 796 | 798 | 801 | 952 | 1012 | 1090 | 34% | 8.4%
Quarterly Enterprise WLAN Market Growth from 1Q11 to 4Q12 (based on estimated revenue)
*Compound quarterly growth rate
SOURCE:

## Slide 7: More is Killing Wi-Fi
1
Interference
3
Flexibility and Scale
2
Capacity Constraints
Dealing with mobile device capacity and management
Product and management solutions for any network
Dropped packets, low data rates
MORE
USERS
MORE
DEVICES
MORE
TRAFFIC
MORE
VIDEO
MORE
HOTSPOTS
MORE
NOISE
MORE
APPLICATIONS
Industry Challenges!

## Slide 8: Technology Breakthroughs
Advanced
per-user
security
Adaptive
antenna
technology
QoS
ChannelFly
SmartRoam
Airtime Fairness
Band-Steering
Self-provisioning self-optimizing
high speed wireless backbone
MESHING
ADAPTIVE
ANTENNAS
SMARTCAST
SECURITY

## Slide 9: Automatic Interference Mitigation
Minimizes Packet Loss and Re-Transmissions, Increases Reliability
Interference mitigated by positioning antenna nulls in specific directions
Avoiding interference delivers more benefits than a stronger signal
  Better throughput
  More predictable connectivity
AP

## Slide 10: Transmit Beamforming
Adaptive Antennas and Transmit Beamforming Working Together
3dB
6dB
9dB
SIGNAL TO INTEFERENCE
PLUS NOISE (SINR)
IMPROVEMENT
>
9dB OF
INTEFERENCE
MITIGATION
15dB OF
>

## Slide 11: BeamFlex+
Better reception (PD-MRC) for weak and hard to “hear” devices
Better transmission to devices constantly changing their orientation
Device orientation accounts for up to 5x performance differential among products
VERTICAL
POLARIZATION
HORIZONTAL
POLARIZATION
5x
Notes: Improved

## Slide 12: Real-Time Adaptation
Interference
Patented technology that combines:
  Smart antenna arrays
  Best path selection algorithms
  Advanced quality of service engine
  Smart mesh RF routing
  Centralized Wi-Fi management
Adapts to real-time changes in environmental conditions
Extends signal range (Wi-Fi coverage) 2 to 4 times with fewer APs
Radically simplifies deployment and administration

## Slide 13: ChannelFly
Predictive channel system
Maintains maximum network throughput
Quickly avoids interference from congested and noisy environments
Feature Summary
Continuously learns network capacity to evolve channel decision intelligence
Evaluates all channels, not just 1/6/11, by using them – no background scanning or guessing required
Fast reaction (in seconds) to significant drop in throughput
Wi-Fi Client friendly using 802.11h
Supports 2.4 GHz, 5 GHz and Mesh
5
1
2
3
4
Channel | 1 | 2 | 3 | 4 | 5
Observed throughput | 80 | 24 | 160 | 30 | 12
…
…

## Slide 14: It’s All About Channel Capacity
2.4GHz RF CHANNEL
OBSERVED THROUGHPUT (Mbps)
TIME (miscroseconds)
0
500
Competing approaches:
Go off channel to listen only
Listen for beacons, frame errors, RF interference
Take a very small snapshot in time
Don’t provide a complete view of the entire spectrum

## Slide 15: Extensive Smart Wi-Fi Portfolio
Entry level 802.11n
3X3, 3-stream dual-band 802.11n
Mid-range dual band
MIDRANGE
HIGH END
Enterprise dual-band
LOW END
Entry-level
802.11g
Wi-Fi wall switch
6 to 50 Aps
SME
50 to 500 APs
Mid-range
50 to 1000 APs
High end
Up to 10K APs
SP Gateway platform
Dual-band 802.11n
Strand mount
802.11n
Dual-band
sectorized
Dual-band AC powered
Small cell + Wi-Fi
Point to point and
multipoint bridges
INDOOR
MANAGEMENT
OUTDOOR

## Slide 16: Questions

## Slide 17: Wi-Fi – Past Present and Future

## Slide 18: Past and Present...
Whiteboard session

## Slide 19: Ruckus on 802.11ac

## Slide 20: An Overview
RUCKUS WIRELESS PROPRIETARY AND CONFIDENTIAL
5 GHz Only
Optimistic Specs
Multi-user MIMO (MU-MIMO)
Breaks “gigabit” barrier
Max of 6.9 Gbps
“Gimmick” specs that drive data rates very high
Many features not practical for real-world enterprises
Encourages 5G adoption
Focuses on capacity-rich, low-interference spectrum
Benefits entire Wi-Fi ecosystem
Up to 8 spatial streams
AP
N-fold efficiency improvement
Increases radio complexity, power draw, and cost
Requires client-side support
Not possible today
Simultaneous downlink Tx to single-stream clients
Multiples network capacity
Key differentiator from 802.11n
5G
2.4G
256-QAM
More efficient modulation
33% data rate gains
Very short ranges only
Requires 11ac clients
80/160 MHz channels
Very wide channels
Primary reason for 11ac’s very high data rates
Ineffective use of spectrum in multi-AP environments
Decreases total capacity
160
40
20
80

## Slide 21: 5 GHz Only
11ac supports 5 GHz frequencies only
  Dual-band devices will support 11n in 2.4 GHz
Focuses on spectrum with more bandwidth, less interference, and better scalability and capacity
Encourages client device suppliers to adopt 5 GHz, to benefit from 11ac marketing, leaving 2.4 GHz as “best effort” spectrum
5G
2.4G
480 MHz
25 channels
83.5 MHz
3 channels
Capacity

## Slide 22: 80 and 160 MHz Channels
11ac devices must support 80 MHz channel width
Optional support for 160 MHz
  Contiguous or non-contiguous (80+80)
Boosts maximum 802.11ac specs
Appeal is for consumers with 1 AP
20 MHz
40 MHz
80 MHz
160 MHz
160 MHz (80+80)
114
38
46
54
62
102
110
118
126
134
151
159
42
58
106
122
155
50
36
40
44
48
52
56
60
64
100
104
108
120
112
116
124
128
132
136
140
153
157
161
165
149
5170 MHz
5330 MHz
5490 MHz
5730 MHz
5835 MHz
5735 MHz
UNII-1
UNII-2
UNII-2e
UNII-3/ISM
802.11a/b/g
802.11n
802.11ac
Red channels are not permitted in some regions
25
12
6
2
2
Total
9
4
2
0
1
144
142
138
DFS
OVERVIEW
Cons
Pros
Max data rate is more than doubled
Boosts throughput in networks with few APs
Improves backup, file transfer speeds
Sub-optimal spectral reuse in multi-AP deployments
Max of 5 non-overlapping 80 MHz channels
Increases neighbor interference and contention
Likely decreases aggregate capacity in enterprise
Notes: New Channel Terminology:
20 MHz - 36, 40, 44, 48, 52, 56, 60, 64, 100, 104, 108, 112, 116,120, 124, 128, 132, 136, 140, 144, 149, 153, 161, 165, 169
40 MHz - 38, 46, 54, 62, 102, 110, 118, 126, 134,142, 151, 159
80 MHz - 42, 58, 106, 122, 138, 155
160 MHz - 50, 114

## Slide 23: Dynamic Bandwidth Operation
Wider channels (80 / 160) have “primary” subchannels (20 / 40 / 80)
Devices can dynamically use smaller or larger bandwidths according to interference (Wi-Fi or non-Wi-Fi) in the larger portions of the band
20
20
20
20
20
20
20
20
40
40
40
40
80
80
160
36
40
44
48
52
56
60
64
UNII-1
UNII-2
Primary subchannels (20, 40, 80) are used dynamically if larger channel is “busy”
36
40
44
48
80
40
20
36
40
44
48
AP1: 802.11ac
Primary(20): 36
Primary(40): 38
80
40
20
AP2: 802.11ac
Primary(20): 48
Primary(40): 46
20
AP3: 802.11n
Channel(20): 40
TIME

## Slide 24: Spatial Streams
Artificially bloats max data rates of 802.11ac
8x8:8 (MIMO)
8x8:8 (MIMO)
Bandwidth | 1ss | 2ss | 3ss | 4ss | … | 8ss
20 MHz | 78 | 156 | 260* | 312 | … | 624
40 MHz | 180 | 360 | 540 | 720 | … | 1440
80 MHz | 390 | 780 | 1170 | 1560 | … | 3120
256-QAM, 800 ns GI
  Business
    Increases AP/client cost
    Increases AP/client size
    Decreases aesthetic appeal
    2x2 APs often meet the business need
  Technical
    Short range for 4+ streams
    More streams require RF “differentiation” (difficult with 4+ streams)
    Adds power draw on APs (PoE power budget) and clients (battery life)
Real-World Barriers
802.11ac defines up to 8 spatial streams
802.11n defined up to 4 spatial streams
Flagship devices today support up to 3SS
Enterprises often prefer cost/performance of 2x2 APs

## Slide 25: 256-QAM
256-QAM
64-QAM
16-QAM
QPSK
BPSK
0
1
01
11
00
10
100% gain (2x)
100% gain (2x)
50% gain (1.5x)
33% gain (1.3x)
256-QAM improves efficiency by 33%
Higher-order modulation adds complexity, which requires higher SNR
  Beneficial near the AP
Efficiency gain from modulation does not increase linearly
Requires 802.11ac AP and client

## Slide 26: Multi-User MIMO (MU-MIMO)
Transmit simultaneous downlink frames to different receivers
Significant capacity enhancements in environments with many single-stream devices (tablets, smartphones)
Requires 11ac client(s) with TxBF feedback/support
Creates new challenges related to signal steering and isolation
  How to get…
4x4:4
Access Point
Stream 1
Stream 2
Stream 3
Stream 4
4x4:4
Access Point
Stream 1
Multi-User MIMO
Multiple downlink Tx at same time
Single-User MIMO
Single downlink Tx at a time
DataA to StaA
DataB to StaB
No DataA to StaB
No DataB to StaA

## Slide 27: Large(r) Frame Size
Payload
MAC Header
PHY Header
Interframe Space
Random
Backoff
Interframe Space
ACK
Overhead
Effective
Overhead
Time
*Note: Diagrams are not to scale and are conceptual only
Payload
MAC Header
PHY Header
Interframe Space
Random
Backoff
Interframe Space
ACK
Overhead
Effective
Overhead
Payload
MAC Header
PHY Header
Interframe Space
Random
Backoff
Interframe Space
ACK
Overhead
Effective
Overhead
11a/g
11n
11ac
Why throughput does not equal data rate…
The Solution: increase payload size
  Every data frame in 802.11ac is an A-MPDU
  Better spectrum efficiency enables larger frame sizes without adverse impact from interference
  Use of large frames depends on high rates
PHY | Aggregation | Max Bytes (Layer 2) | Max Bytes (Layer 1)
11b | N (fragmentation often used) | 2,304 | ~2,336
11a/g | N | 2,304 | ~2,336
11n | Y | 7,935 | 65,535
11ac | Y | 11,454 | 1,048,575

## Slide 28: FAQ
Is it backward compatible with 11a/n?
Yes. 11ac is fully backward compatible with 802.11a/n, using protection mechanisms with 11a/n frame formats.
What about 2.4 GHz?
Initially, dual-band APs will be 802.11n in 2.4G and 802.11ac in 5G. 11ac may eventually be retrofitted to 2.4G for benefits from added spatial streams or 256-QAM.
Will it require new hardware?
Yes. For every supplier, all APs and clients will need new hardware, whether complete AP replacement or modular radio add-ons. Controllers or management software may be software upgradeable.
Q:
A:
Q:
A:
Q:
A:

## Slide 29: 11ac in Waves
Net gain
  Slight efficiency improvement, most benefits are for 802.11ac devices
Wave 1 – Q3, 2013
256-QAM | 33% gain at very short range
80 MHz channels | Twice the capacity of 40 MHz 802.11n (but not recommended for multi-AP deployments)
3 spatial streams | Already supported by 802.11n (3x3)
Net gain
  Multiples aggregate network capacity and efficiency, ALL devices benefit
Wave 2 – Late 2014
Wave 1+ | Includes all Wave 1 features, with additional chip improvements
80 / 160 MHz channels | Twice the capacity of 80 MHz 802.11ac (but not recommended for multi-AP deployments)
3+ spatial streams | Likely 4 spatial streams. N-fold throughput gain for high-end clients, more flexibility/capacity for MU-MIMO
MU-MIMO | Up to 4x capacity boost, multiplies aggregate capacity

## Slide 30: Better 11ac with Ruckus
Making the most of next-generation Wi-Fi
RUCKUS WIRELESS PROPRIETARY AND CONFIDENTIAL

## Slide 31: Maximizing 256-QAM
BPSK
DPSK
16-QAM
64-QAM
256-QAM
With per-packet adaptive antenna control, polarization diversity, and active channel selection techniques, Ruckus APs maximize the potential of 256-QAM with 11ac
  Greater SNR/SINR increases the useful downlink range of 256-QAM
  Adaptive PD-MRC and higher uplink receive sensitivity increase uplink range of 256-QAM
  APs select channels with more capacity and less noise and interference
Them
Us

## Slide 32: Smarter Channel Planning
38
46
54
62
42
58
50
36
40
44
48
52
56
60
64
36
40
44
48
TIME
CHANNEL PLANNING
DYNAMIC OPERATION
CHANNELFLY
802.11ac introduces the possibility of 20 MHz, 40 MHz, 80 MHz, or 160 MHz channels
Each 40, 80, or 160 MHz channel will have primary 20, 40, and 80 MHz channels
It becomes increasingly difficult to determine what channel widths are optimal for each environment based on spectral reuse, the number of APs, transmit power, client device types and channel support, etc.
Manual channel planning becomes VERY DIFFICULT
The dynamic nature of RF environments raises new concerns for both ongoing channel width settings (should we use 20s, 40s, 80s?) as well as AP channel assignment adaptation (what primary 20/40/80 channels should I use at any moment in time?)
APs must be able to select the best primary 20, 40, and 80 MHz channels for their own environment, or possibly change from 80 MHz operation to 40 MHz.
ChannelFly will tackle both problems (channel width and channel assignment) by…
  Actively measuring performance on each channel
  Adaptively changing as environmental conditions fluctuate
  Discovering the best channel settings for the environment, the client device types, count, and channel width support, and the amount of traffic at each bandwidth setting

## Slide 33: BeamFlex-Enhanced MU-MIMO
Antenna 2 to Client 2
Antenna 1 to Client 1
Antenna 3 to Client 3
AP
3x3 MU-MIMO
3 clients concurrently communicate with AP, each on a dedicated spatial stream (and antenna)
MU-MIMO enhanced with BeamFlex
Directional antenna element for each client
Better signal separation
Higher sustained data rates
Increased AP capacity
Standard MU-MIMO
All clients hear all antennas
Poor signal isolation per client
Lower SNR per link = lower data rates
Marginal benefit to capacity
Notes: Each antenna achieves directivity adapted individual clients, so each client hears its dedicated antenna best

## Slide 34: 11w Overview
Ratified by IEEE in 2009 (802.11w-2009)
Introduced by Wi-Fi Alliance as Protected Management Frames (PMF) certification
Deauth / Disassoc.
Invalid. Disregard.
HACKER
Deauth / Disassoc.
VALID USERS
OK
OK
HACKER
PRIOR TO 802.11w
WITH 802.11w
Invalid. Disregard.
✔
OK
✔
VALID USERS
Invalid. Disregard.

## Slide 35: Frame Types w/o 11w - Primer
✔
Mgmt
Control
Data
802.11 FRAME TYPES
Beacons, Probes, (De)Authentication, (Dis/Re)Association, Action
No encryption, data origin authentication, or replay protection
Easily spoofed, enabling hijacking, DoS, and many other attacks
RTS, CTS, ACK, PS-Poll
No encryption, data origin authentication, or replay protection
No protection needed
Data, Null Data, QoS Data
Provides encryption, data origin authentication, and replay protection
Unicast protection uses individual PTK
Group (BC/MC) uses shared GTK
Traditionally, only data frames are encrypted and integrity-protected (source validation)
Management frames are increasingly important to network operation
802.11w provides for data integrity, replay protection, and origin authenticity of some management frames
  Robust Management frames – Disassociation, Deauthentication, and Robust Action frames
PROTECTED

## Slide 36: How it works
Security keys are negotiated at association
  If PMF is supported, unicast frames (data and mgmt) are protected with CCMP/AES
  Group protected management frames rely on Broadcast/Multicast Integrity Protocol (BIP), which also use
11w provides data integrity and replay protection for robust management frames
Detects whether received frame is an unauthorized retransmission
11w Protected Frames
802.11 header
Management Frame Body
MMIE
Management MIC IE (MMIE) contents
  KeyID – Identifies the IGTK (unique to sender) used to compute MIC
  IGTK Packet Number – Sequence counter used for replay protection
  MIC – Message Integrity Code calculated over frame body
FCS
ADDED IN 11W
Type | Unicast | BC/MC
Data | TKIP/CCMP (PTK) | TKIP/CCMP (GTK)
Control | None | None
Mgmt | None | None
Robust mgmt | CCMP (PTK) | BIP (IGTK)

## Slide 37: Limitations
Robust management frames are NOT encrypted
  They are still sent “in the clear”
Does not provide data origin authenticity (can I confirm who sent this?) to bc/mc frames (data and mgmt – fault of symmetric encryption)
Does not help clients that do not support 11w – they still need traditional unprotected management frames
  PMF can be “mandatory” or “supported”
  If “supported,” only clients with 11w support have protection
Deauth / Disassoc.
VALID USER WITH 802.11w
Invalid. Disregard.
HACKER
PMF “SUPPORTED”
Invalid. Disregard.
✔
VALID USER NO 802.11w
OK

## Slide 38: HotSpot 2.0 and the Enterprise
Provider leverages hotel infrastructure for data offload/extended service footprint
Provider increases visibility and stickiness to subscriber (loyalty)
Provider SSID enabled on any/all APs
Provider SSID tunneled to 3G/4G core (transparent authentication, policy, etc.)
Hotelier enables Wi-Fi mobility for dual-mode handsets
Hotelier adds incremental revenue at no cost
Hotel
SSID
HS2.0
SSID
PROVIDER DATA CENTER
Secure tunnel to provider NOC/DC
Offload directly to Internet
3G/4G
Cores
INTERNET

## Slide 39: Questions
Break

## Slide 40: High Density Wi-Fi
Design and Technology

## Slide 41: High Density Defined
A high density deployment generally has:
  More than 3 APs required to support SLA
  Very few physical obstructions
  High number of concurrent users

## Slide 42: High Density Challenges
The Unbounded Medium
Number of devices per channel
Number of available channels
Co-channel interference

## Slide 43: Co-Channel Interference
Notes: 43

## Slide 44: Co-Channel Interference
*Circle represents > -70 dBm
*Circles represent > -95 dBm
Notes: 44

## Slide 45: Somewhat Bold Statements
The more obstructions, the better
Extra signal from adaptive antennas isn’t as advantageous as usual
Hope that the customer wants a lot of downstream traffic

## Slide 46: The More Obstructions is Better
High density areas are prone to co-channel interference
Obstructions attenuate RF energy and significantly reduces co-channel interference

## Slide 47: Extra Signal From Adaptive Antennas Isn’t as Helpful
Excess signal actually creates more problems than it solves in HD scenarios.
Most vendors control their signal by reducing transmit power
However, control of the signal is key.
  Adaptive antenna array sends the signal only where it needs to go

## Slide 48: Co-Channel Interference reduction with BeamFlex
Ch 1
Ch 6
Ch 11
Notes: 48

## Slide 49: Hope That The Customer Wants A Lot Of Downstream Traffic
Downstream traffic is only sent by the AP
Upstream traffic is sent by everyone else
  The more devices that transmit, the higher the chance of collision

## Slide 50: Data rate, Signal and Capacity
Example RSSI Chart
  180 Mbps = -82 dBm
  240 Mbps = -78 dBm
  270 Mbps = -76 dBm
  300 Mbps = -74 dBm
Channel Capacity Improvement
  + 8dB = 50.3%
  + 4dB = 18.5%
  + 2dB = 8.2%
Higher signal equals higher data rate
Higher data rate equal higher capacity

## Slide 51: Airtime Fairness
The Problem
  Diversity of clients
    Slow vs. fast clients
    11b vs. 11a/g vs. 11n
  Slower clients take more air-time and slow-down faster clients
    Effectively, all clients are limited to the slowest client throughput
    Overall WLAN performance degrades
The Solution
  Schedule transmit queues subject to airtime constraints per STA
How it Works
  Weighted round robin
    Per client queues, weighted round-robin (but with equal weights…)
    Frame aggregation is a special case  11n clients do get some preference
  11n-only mode – keep 11a/b/g clients out of the WLAN

## Slide 52: Real World Results
BEFORE
AFTER
Multi-rate testing with clients
  11n and 11a clients
  High data rate 11a and low data rate 11a clients
  High data rate 11n and low data rate 11n clients
802.11a stations continue to operate at expected levels
802.11n stations experience much higher levels of throughput with airtime fairness enabled
Performance of both 802.11n and 802.11a stations without airtime fairness enabled

## Slide 53: Dealing With Density
Dual-band
802.11n
Steers clients to 5GHz by withholding probe and auth responses on 2.4GHz
Does not steer clients below RSSI threshold set per WLAN
Client table in each AP tracks
  Client probe requests per band
  Avg. RSSI per band over last minute
  Dual band support
Table checked before responding to client
After Band Steering
5GHz – 14 (82%)
2.4GHz – 3 (18%)
Band Steering for High Capacity Environments
Before Band Steering
5GHz – 3 (18%)
2.4GHz – 14 (82%)
2.4 GHz
5 GHZ

## Slide 54: ChannelFly
predictive capacity management technique
Maintains maximum network throughput
Quickly avoids interference from congested and noisy environments
Feature Summary
Continuously learns network capacity to evolve channel decision intelligence
Evaluates all channels, not just 1/6/11, by using them – no background scanning or guessing required
Fast reaction (in seconds) to significant drop in throughput
Wi-Fi Client friendly using 802.11h
Supports 2.4 GHz, 5 GHz and Mesh
5
1
2
3
4
Channel | 1 | 2 | 3 | 4 | 5
Observed throughput | 80 | 24 | 160 | 30 | 12
…
…

## Slide 55: It’s All About Channel Capacity
2.4GHz RF CHANNEL
OBSERVED THROUGHPUT (Mbps)
TIME (miscroseconds)
0
500
Competing approaches:
Go off channel to listen only
Listen for beacons, frame errors, RF interference
Take a very small snapshot in time
Don’t provide a complete view of the entire spectrum

## Slide 56: What does 802.11h do?
Coordinated channel changes w/out service interruption
  Change announced in advanced and synchronized with beacons
Clients
  Extremely fast change but does varies from chip to chip
  Packets buffered at AP, no loss
  Supported by all 5 GHz clients
  Supported by most 2.4 GHz clients (Apple, most Android, Qualcomm, Atheros, Broadcom, …)
Mesh
  Packets buffered so no packet loss as mesh tree is synchronized
ChannelFly uses 802.11h channel change announcement

## Slide 57: Why Ruckus is Better at HD
Performance is dictated by channel usage
Adaptive antennas provides better control of the medium
  Fewer devices contending for the same channel
Maintaining higher data rates increases channel efficiency
It’s just physics

## Slide 58: Questions
Lunch time

## Slide 59: Tools & Mobile Apps
What to use and how to use it

## Slide 60: Tools
Wireshark
  Remote and local packet captures
Metageek
  Wi-Spy
  EyePA
  InSSIDer
NetSpot
  Discovery / Site Survey (basic, Mac only)
Wi-Fi Explorer
  Discovery tool (like InSSIDer for Mac)

## Slide 61: Wireshark
Go to Edit/Preferences/Capture
Select "enX" interface
Select "monitor mode"
In the "Default link-layer header type", select with ”Per-Packet Information” header.
Select "OK", then you can capture natively
Capture natively on Mac
Capture with AIRPCAP on Windows

## Slide 62: Mobile Apps
S.W.A.T. (SpeedFlex Wireless Assessment Tool)
  Site survey companion
SpeedFlex
  Mobile throughput test tool
Zapper
  Competitive and performance analysis tool (CDF generator)
ZoneDirector Remote
  Real time monitor of your ZD

## Slide 63: S.W.A.T. for iOS and Android
57%
Throughput based analysis
Project and survey creation
Import floor plans via popular cloud service Dropbox
Snap a quick photo with the built in iPad camera
Locate floor plan from photo gallery
Scale floor plan to make heat map more accurate
Choose from most common Ruckus APs
Test throughput by UDP/TCP, uplink and downlink
Generate email with throughput and/or heat map results
Upload heat map results to Dropbox
Wireless performance testing and site survey companion

## Slide 64: SpeedFlex for iOS and Android
Real time mobile performance testing
Throughput based analysis
Instantly attach core location data to results (GPS)
Test throughput by TCP/UDP and UP/DOWN
Packet loss percentages
Generate email with results and location data

## Slide 65: SpeedFlex (Android)
RSSI
Google Maps
Wi-Fi Channel
Frequency

## Slide 66: Zapper (iPad)
57%
18%
10%
15%
Wi-Fi performance analysis tool
Perform real time throughput testing and instantly results graphed
Built on open source ZAP library
CDF (cumulative distribution function) shows identifiable metrics that indicate performance fluctuations
Allows product and competitive testing
Multiple tests with combined test view
Uplink or downlink testing
Email the results, including spreadsheet of results
Competitive comparisons, AP validations or general site verification

## Slide 67: ZD Remote (iPad)
57%
18%
10%
15%
Real time ZD monitoring capability
Real-time monitoring of Ruckus ZoneDirector
Provides dashboard view with easy to understand widgets such as
  System overview
  Device summary
  Usage statistics
  Currently active clients
  Client device types
  Live logs
A single or multiple ZoneDirectors can be administered via application
Select configuration controls (eg. WLANs) coming soon

## Slide 68: Spectrum Analyzer (coming late 2013)
57%
18%
10%
15%
iPad Spectrum Analyzer
FFT (instantaneous, and decaying max hold)
Spectrum CDF / Density (intensity of color shows how often a particular freq/power is observed)
Spectrogram (sometimes called waterfall, shows FFT over time, with color mapped to dBm)
Duty Cycle (by frequency, threshold is adjustable)

## Slide 69: Questions

## Slide 70: Beamforming vs. Adaptive Antennas
Hint: They aren’t the same!
Whiteboard session

## Slide 71: Questions
Break

## Slide 72: Packet Capture & Spectrum Analysis
Remote capture and ideas for troubleshooting
Live Demo

## Slide 73: Questions

## Slide 74: Beyond the Connection
BYOD and the Bonjour Gateway

## Slide 75: Ruckus BYOD Solution
IDENTIFY
  Application Recognition
  Client Fingerprinting
MANAGE
  D-PSK limits per user
  Extended Language Support
  Bonjour Gateway
  MDM
ONBOARD
SECURE
  Secure LDAP
  Application Policy Control
  Enhanced Roles
  On-boarding portal
    Guest Access
    Device Registration
  Mobile Friendly portal
  Customizable Portal Pages

## Slide 76: Key Technologies
Notes: Overview presentation + detailed notes

## Slide 77: What it Looks Like
WHAT HAPPENS WHEN?
Internet
Guest
New BYOD Devices
Provisioned BYOD
Guest
User
Database
Student
Resources
Staff
Resources
Guest
Resources
Student SSID
Student
Staff SSID
Guest SSID (hotspot)
Onboarding SSID
1. Users connect to a provisioning SSID and are re-directed to an onboarding portal.
Users enter domain credentials which are verified against a user database.
3. The user’s role assignment and permissions are automatically determined based on authentcaion.
4. Using Zero-IT, the device is auto-provisioned with a dynamic pre-shared key and dynamically assigned to the requisite WLAN.
5. Devices re-connect on a secure WLAN, receiving network permissions according to their role.
Staff

## Slide 78: Zero IT Automates Onboarding
Requirement: automatic, secure authentication and roaming
Enabled by SSID and authorization protocol configuration
Easy-to-use Ruckus approach to push configuration
Uses mobile OS auto-detect and -authenticate features, not a separate connection manager app
Invitation
Branded Landing Page
‘One-Click’ Configuration
Automatic Authentication Enabled
Notes: Web

## Slide 79: On-Boarding Portal
BYOD SSID
(open)
Proceed to unencrypted
internet on BYOD SSID
Install Client Profile
DPSK/802.1x
Role based SSID
Move Client to
Secure SSID
Traditional Guest Access
Easy BYOD Registration
Single SSID for Guest Access & BYOD Registration
Limit DPSK generation per user
A modern day, mobile friendly, easy-to-use Wi-Fi connection option

## Slide 80: D-PSK Automates Security/Config
WLAN profile configured device, and on the WLAN based on allowed by role.
LDAP sends user security group information to ZD
ZD applies role,
generates D-PSK
pushes dissolvable PROV file to device

## Slide 81: Client Fingerprinting
Visibility “Who’s device is this?”
Self-registration
  Automatically registers and maintains client info on WLAN and Wired interfaces
    Operating System
    Operating System Hostname
Control by device type
  Permit/allow
  Assign to VLAN
  Rate limit (Down/Up)
Management
  WLAN controller or standalone
    WLAN dashboard
    Client monitor
    Client details
Hostname: Dave’s iPhone
    MAC: 50:ea:d6:7c:30:e4
Notes: Web

## Slide 82: Device Specific Policy Enforcement
    Segregates trusted and untrusted devices on single SSID
    Simplified access rules per device
       Windows  Windows Mobile
       Mac OS  iOS
       Linux  Android
       VoIP  Gaming
       Printers
    Control network access per device
    Permit/Deny
    Assign to VLAN
    Rate Limit (Down/Up)
Device Type | Access | VLAN | Rate Limit DL¦UL
Gaming | Deny | - | -
Windows, Mac OS, Linux | Permit | 20 | -
iOS, Windows Mobile, Android | Permit | 10 | 4 Mb ¦ 1 Mb
✖
VLAN 20
VLAN 10
Device Policy Access Control

## Slide 83: Bonjour Gateway – In Phases
FileSharing
Printing
AP Fencing
Fencing*
Bridging
Teacher
VLAN
Student
VLAN
Filtering
Bridging
Filtering
ZD must see all VLAN traffic to provide bridging services.
9.7
9.8
9.7
9.8

## Slide 84: Bonjour Gateway
Demo overview
ZoneDirector and AP setup
Deployment Considerations
Caveats and Limitations
  ZD must be trunked with direct access to all bridged Bonjour services/VLANs
  SSIDs must have static access VLANs (no dynamic VLAN support)
SSID: Staff
VLAN: 110
SSID: Student
VLAN: 120
Router
DHCP Server
VLAN 110, 120
ZoneDirector
Trunk Port
VLAN 110, 120
L2 Switch
VLAN

## Slide 85: Questions

## Slide 86: Competitive

## Slide 87: Independent test results
WI-FI STRESS TEST
20
18
16
14
12
10
8
6
4
2
0
20
30
40
50
60
70
80
VIDEO ERRORS
AVG. TCP THROUGHPUT
Juniper 532
Cisco 3602i
Aerohive AP121
HP 430
Aerohive AP330
Cisco 2602i
HP 460
Xirrus 4820
Aruba 105
Aruba 135
Ruckus 7982
Highest, most reliable performance
Lowest, least reliable performance
Meraki MR24
Meraki MR16
Ubiquiti UniFi Pro
Linksys EA4500

## Slide 88: Independent test results
Chart: 
| 1st Qtr | 2nd Qtr | 3rd Qtr | 4th Qtr
Sales | 66 | 14 | 12 | 2.3 | 5.7
Percentage of Vendor Test Wins
(87 tests)
Industry’s First 3x3:3 802.11n Competitive Testing
66%
14%
12%
2%
6%

## Slide 89: Ruckus Labs
Who is here, What is here, examples.

## Slide 90: Who is here
Marcus Burton
Chandan Argawal
Jim Stewart
Jeanette Lee
Deepak Sant
Dave Wright

## Slide 91: What is here
Ruckus internal test bed
  Performance
  Interoperability
  Competitive
  Best practices
15,000 sq. foot facility
Office park/office environment
  Outdoor testing up to 300m (1,000’) LoS
  300+ Wi-Fi devices … and growing!
  iPads, Phones, laptops, tablets (wide range for testing)

## Slide 92: Questions

## Slide 93: New Products and Features

## Slide 94: Release 9.6
Wireless and Network
  Onboarding Portal (BYOD + Guest Access)
  Per user D-PSK limits
  USB Backhaul “Our-Fi”
  Spectrum Analysis
  Ethernet Jumbo frame support for 7782
  54 SSID per Access Point (27 per radio)
  Tunnel QoS Config (static, copy from packet)
Management
  Syslog Enhancements (Config facility, Add Severity)
  Alarms, Email, Traps sent after reboot
  ZD Ethernet Port Status (GUI, CLI, SNMP, FM)
  FlexMaster Vmware support and Virtual Image distribution
  FlexMaster CentOS support
Products
  ZoneFlex 7055 Wall Switch AP
GA – April 2013

## Slide 95: Introducing ZoneFlex 7055
802.11a/b/g/n, dual-band concurrent 2x2:2
600 Mbps theoretical PHY rate
Gigabit Ethernet Uplink with PoE input (802.3af/at)
Supports SmartMesh Networking
Universal form factor & mounting bracket mounts to worldwide standard utility wall-boxes
Torx screw security against opportunistic theft
(4) 10/100 Ethernet Ports
(1) 802.3af PoE output
Pass-through support
Support ZD/FM 9.6, SCG 2.1
Now Shipping with 9.6 LCS Support
Industry’s first dual-band concurrent 2-stream wall-plate AP

## Slide 96: SmartPoint USB Backhaul
Carrier Class Mi-Fi
Utilize USB interface on AP for network backhaul
    3G/LTE/WiMax
Backhaul for Mesh & Ethernet
Monetize Spectrum
Quick & Easy Deployments
Requires special order AP (USB + Filters)
Purchased Spectrum: 3G/LTE/WiMax
Carrier Network
AP
ZD/SCG
USB Dongle
LWAPP/GRE Tunnel
Carrier Network
Hot Spot/3G/LTE by Carrier or Mobile Operator
Retail, Restaurant, Business Kiosk, Temporary Networks

## Slide 97: Spectrum Analysis
Real-time spectral analysis
  ZD GUI
  Hi-Res iPad App (2H 2013)
Visualize and investigate interference from Wi-Fi and non-WiFi sources.
Remotely accessible via network
Available on:
  7055, 7321, 7352, 7372,7982, 7782, 8800
ZD GUI
iPad App
Visualize & Investigate
Sources of Wi-Fi & non Wi-Fi interference

## Slide 98: Release 9.7
Wireless and Network
  WIPS Enhancements (Manual Contain, Signal Strength, OID of Rogue, Display Malicious Only)
  SmartClient single redirection support
  Force DHCP on WLAN
  Bonjour Gateway
  AP Survivability for New Associations with Open/WEP/PSK
  Full L2 Client Isolation
  Ekahau BLINK support
Management
  Channel Fly Memory/Reset
  DHCP for Smart Redundancy
  Polycom Compatibility auto-config
Beta – May 2013
LCS – June 2013
GA – July 2013

## Slide 99: WIPS Enhancements
Show RSSI of top 5 reporting Access Points
Manual Containment & Display of “user-blocked” devices
Limit rogue reporting by Malicious Rogue type
  Event-log, SNMP trap, syslog, e-mail
Filter GUI by malicious only
Limit Rogue Reporting
Detecting AP with signal strength
Filter GUI by malicious type only
Manually Contain

## Slide 100: AP Survivability
Enables existing and new client connectivity when ZoneDirector is offline
New Autonomous WLAN
  Auth type: open
  Encryption type:
    WPA, WPA2, WPA-Mixed, WEP-64, WEP-128, None
No Tunnel Support
ZD GUI/CLI support

## Slide 101: ZoneFlex R700
Phase 1 802.11ac Indoor Access Point
802.11a/b/g/n/ac 3x3:3 Concurrent Dual-Band
  802.11b/g/n 2.4 GHz radio  450 Mbps theoretical PHY
  802.11a/n/ac 5 GHz radio  1,300 Mbps theoretical PHY
BeamFlex adaptive antennas
  21 switchable elements provide 3,000+ unique patterns
  Dual polarity
2x Gigabit Ethernet Ports
Powered by 802.3af/at or 12VDC wall adapter
Dimensions: 15.8 x 15.8 x 4 cm (7982 form-factor)
Availability (plan of intent)
Shipping 2H 2013

## Slide 102: Questions